## Slide 1: Recent status of the NANTEN2 and Nagoya project
Hiroaki Yamamoto
NANTEN2 project, Nagoya University
NANTEN2 workshop @ Adelaide 2014.2.3-4
Image:
Pampa la Bola @ 4865m
NANTEN2 with Milky Way

## Slide 2: Members contributed from Japan
Nagoya University
- Staff: Y. Fukui, K. Tachihara, H. Yamamoto
A. Mizuno, T. Nakajima
- Posdoc: T. Hayakawa, K. Torii, T. Kuwahara
- PhD students: 6, Master course: 5
Osaka Prefecture University
- Staff: Hideo Ogawa, Toshikazu Onishi
- PhD student: 1

## Slide 3: Contents
NANTEN2 project
- Timeline, Facility, Site, Instruments,
History in 2013, Weather
Results with Nagoya Receiver
NASCO receiver
Progress on NASCO system

## Slide 4: Project Timeline
2004.8: Move to Pampa la Bola from Las
Campanas Observatory
2005.9: First light in mm
2006.4: First light in Sub mm
2007.10: Start remote observations
2009.4: Install of SMART
2014.late: Install of NASCO

## Slide 5: View of area
Alt. 2400m
Alt. 2900m
Alt. 5100m
Alt. 4800m
ALMA Gate

## Slide 6: Facilities
・Sequitor Basecamp
・Don Esteban Basecamp
©2005 Astro-Norte.
・ For only Japanese
・ Inside is Japanese style
・ 3 rooms, max 6 people
・ Satellite connection
・ Cook by ourselves
・ For German, Australian etc
・ Use other groups as well
・ Satellite connection
・ dining room etc

## Slide 7
Atmospheric
Observation
Dome
Rest, observation
Weather monitor, Old AOS system etc
Principal branch
of the power
Experimental room, tools
warehouse
Old 4m dish
Satellite
antenna
Fuel tanks
(15,000L x 2)
Generator house

## Slide 8: Observable Sky from the NATNEN2
Galactic Longitude
Galactic Latitude

## Slide 9
Sub-ref
Main dish
Tertiary mirror
Fourth mirror
Fifth mirror with wire grid
Sixth mirror
SMART
115GHz receiver
Cabin
SMART
Nagoya RX
SMART
Nagoya
Cold load
NANTEN2 Optics

## Slide 10
NANTEN2 Instrumentation
230GHz receiver
1 pixel, DSB receiver
4-8GHz IF
2 DFS, 1GHz width and 61kHz resolution for each
Observations of 12CO(J=2-1) and 13CO(J=2-1),
or 13CO(J=2-1) and C18O(J=2-1), simultaneously
500/800GHz receiver (SMART)
8 pixels for each frequency
Observation in 500/800 GHz simultaneously.
AOS, 1 GHz width and 500kHz resolution for All pixel
DFS, 1.5GHz width for each

## Slide 11: 2013 timeline
2013
End of January: Generators arrive at ATF.
End of February: Generators arrive at PLB.
Late March-Early April: replacing the generators
Middle of April: Start to an operation
Middle of May: Snowing, impossible to access the site for 10 days
Middle of June: Snowing, impossible to access the site for 5 days
Middle of July: Snowing, impossible to access the site for 1 week
Early August-End of December: Scientific Observations
2014
January: Maintenance of Dome, Telescope and 230GHz system

## Slide 12: Replacing generators

## Slide 13: 2013.5.27
2013.6.17

## Slide 14: 2013.7.23-29

## Slide 15: 2013.7.29-30

## Slide 16: Weather Status in 2013
Generators, snow, weather condition
From APEX web site
PWV=1.0mm
27.8%
12.2%
40.6%
19.4%
Full year PWV distribution 2013
Acumulated 2013
PWV < 1mm 30%, PWV < 1.5mm 40%, PWV < 5mm 60%

## Slide 17: Targets in 2013
Objects in the Galactic Center
SNR: IC443
Massive Star Forming Region: RCW38, RCW120
Los Mass Star Forming Region:
High Latitude: Pegasus Loop, B=-70

## Slide 18: NAnten Super CO survey (NASCO)
Survey Name | Coverage (deg) | HPBW (‘) | Grid (‘) | Vel cov. (km/s) | Vel reso. (km/s) | RMS[K]@ 1km/s reso. | Total points (million)
NGPS | 200<L<60,B<¦10¦ | 2.6 | 4-8 | ±300 | 1.0 | ~0.35 | 1.1
NASCO | 70% of sky | 2.6 | 1 | ±1300 | 0.16 | ~0.2 | 20
New Survey by NANTEN2 in 12CO and
13CO(J=1-0) simultaneously.
Survey beyond NGPS
Covering 70% area of whole sky
Unobservable
from NANTEN2

## Slide 19: System of NASCO
4 beams receiver: DSB mixer with OMT
3 beams for 115GHz and 1 beam for 230GHz
4-12GHz IF for 115GHz and 4-8GHz IF for 230GHz
Back-ends will be shared with SMART
4 beams x 2 polarizations x 2 lines (12CO and 13CO)
 16 IFs in total

## Slide 20: New Optics
Expected Antenna pattern
NASCO receiver
Making by 3D printer in University’s machining center

## Slide 21: Simulation of Observations
3 beam of
115 GHz
1 beam of
230 GHz

## Slide 22: The 2014 Season
Start an operation in April
230GHz receiver is continue to use
Late 2014, we will install NASCO receiver.